## Slide 1
Title : Flash Upgrade, Sigma Studio Plus
24 Oct 2024

## Slide 2
A firmware update is the process of upgrading the firmware installed on a device by altering its code. Firmware updates typically come from the device manufacturer and are designed to fix bugs, improve performance, enhance security and introduce new features.
How to update firmware depends on the device, and updates can be delivered through various channels,
  Over-The-Air (OTA) through wi-fi/ Bluetooth.
  USB connections using USB storage devices.
  through computer software provided by the manufacturer.
Firmware update and Purposes

## Slide 3
Audio applications such as AVR and Soundbar use flash devices where the audio processing modules binary image is stored. This binary image is loaded into the DSP during the booting process and executes from DSP in run time.
This .wav file will be played back through HDMI using any audio pumping device and the DSP will be configured (Command A) to take the Audio application loader content and write into the Flash memory space.
Firmware update via HDMI

## Slide 4
Flash Writer Mode – Before Flashing

## Slide 5
Flash Writer Mode – After Flashing

## Slide 6
Application Mode

## Slide 7
Upgraded DSP Firmware working status

## Slide 8
Sigma Studio Plus
The SigmaStudio®+ graphical development tool is the programming, development, and tuning software for the SHARC® audio processors
SigmaStudio Plus includes an extensive library of algorithms to perform audio processing such as filtering, mixing, and dynamics processing, as well as basic low-level DSP functions and control blocks. Plug-in algorithms from Analog Devices and 3rd party partners can be added to SigmaStudio's drag-and-drop library

## Slide 9
Software Required:
Cross Core Embedded Studio [CCES v2.9.1 or Later]
SigmaStudio+ [2.1.0 or Later]
Hardware Required:
ADSP-21569 EZ BOARD
Eval Melody-8 (ADSP-21569)
EVAL-ADUSB2EBUZ (USBi)
Software and Hardware Requirement

## Slide 10
Hardware Connections
ADSP-21569-EZ-KIT

## Slide 11
SS+ Graphical Development Environment

## Slide 12
Sigma Studio Plus on Jasmin GUL SDK

## Slide 13
Sigma Studio+ Design Mode

## Slide 14
Sigma Studio+ Deployment Mode

## Slide 15
SigmaStudio+ [Analog Devices Wiki]
ADZS-21569-EZKIT Evaluation Board | Analog Devices
EVAL-MELODY-8 Evaluation Board | Analog Devices
SHARC Processors Software and Tools | Analog Devices
https://youtu.be/DX8qS3dbtmE?si=g4DUcTda0zJW6Gp9
References

## Slide 16
Prepare SigmaStudio+ Schematics with the following feature.
  8 channel input
  2 channel output (8 channels are mixed to create stereo effect).
  Include mute option for each channel.
  Include eight band equalizer to control the effect of stereo output channels (Band Freq : 200Hz, 2KHz, 5KHz, 8KHz, 10KHz, 12KHz, 14KHz & 16KHz).
  Include White noise and route the noise signal into 2 channel output if required, using switchable option between noise and audio signal.
How does Flash Upgrade work?, based on your understanding list down step-by-step procedure with your own words.
Task and Activity

## Slide 17
THANK YOU!
India, Germany, Japan, USA & China
+91 44 6666 9600
www.jasmin-infotech.com