## Slide 1
Audio Framework (Autodetection, Buffer flow, Data flow)
Mukeshkumar M
Ajithprabhu ST

## Slide 2
HDMI
DAI
SPORT
Rx
DMA
Rx Buffer
Auto Detection
Pack
Buffer
Check
Valid
Decoder
Post
Processing
Predac
Buffer
DMA
Tx Buffer
SPORT
Tx
DAI
CODEC
Audio O/P
NO
YES
Audio Framework Basic Flow
Wait for next data from receiver

## Slide 3
Realtime Framework – Buffer Flow
3
3
Rx DMA
Auto Detection
Decoder
Pack Buffer
SINGLECORE
Post Decoder
Predac Buffer
Processing buffer
Processing buffer
TX DMA
Customer PP
Processing buffer

## Slide 4
Pack Buffer:
    Is an input buffer which receives the samples from Auto detection.
    Pack buffer size in the framework will be Sample block * No of input channels * No of Halfs.
    The sample block and Number of Half's will vary based on decoders.
    This works in a circular fashion.
    When the Pack is filled, This will be sent to next flow i.e, Decoding
Predac Buffer:
    Is an output buffer which gets the output samples from the decoder.
    Predac buffer size in the framework will be Sample block * No of Output channels * No of half
    Factors like the Number of Cores and decoder latency decides the Number of Half.
    This works in a circular fashion.
    When the Predac is filled, This will be sent to next flow i.e, Transmitter.
Processing Buffer:
    Is an internal buffer used to store the intermediate results.
    Size of the buffer is usually sample block * No of input channels
    This can be reused in the audio chain
<number>
Realtime Framework – Buffer Flow
Processing Buffer
Predac Buffer
Pack Buffer

## Slide 5
Input / Output Data flow of the audio framework includes
    Sample block : 256 , 128
    Bit Rate : 24 bit / 32 bit
    Data Format : Floating / Fixed
    Data Organization:
    Block based - Processes data in larger chunks or blocks.
    Interleaved - Combines multiple channels into a single stream.
When Factors copying the Data between buffers
    Source and Destination Buffer pointers
    No of samples to be copied
    Buffer Stride
Circular Pointer update :
Whenever a data copied to or from a circular buffer, the respective read and write pointers to be updated for the next processing
Empty Space and Filled Space checking:
This is to check a valid sample is available to process and enough space is available to fill data
Realtime Framework – Data Flow
Interleaved format
Block based format