## Slide 1: SHARC ASM Coding Guidelines
Proprietary and Confidential

## Slide 2: WHY C?
Advantages:
Removes the problems of manual coding (Especially Errors)
Provides a level of Platform independence
Quick time to market
Ease of upgrade
Disadvantages:
Not as optimized as assembly implementation
Requires an amount of compiler knowledge (i.e. How the compiler translates / interprets the High level language code) to achieve a good level of optimization
Proprietary and Confidential

## Slide 3: WHY ASM?
Advantages:
More Optimized code
Complicated loops are modified to enable simd using asm.
Disadvantages:
Need to save and unsave registers
Difficult to develop compared to c
Proprietary and Confidential

## Slide 4: CONTENTS
Proprietary and Confidential
Declaration in C and ASM
Naming Conventions
Function calls
Guidelines to be followed during Function calls
Argument Passing
Memory section definitions

## Slide 5: Declaration in C and ASM
The data type of the variable should be mentioned correctly while declaring any variable.
Eg: int example; unsigned int example.
Eg: In C In Asm
int test; .var temp.;
int array[10]; .var buffer[10];
Question: How do you manage various formats (Int, Uint, float etc) in Asm ?
Proprietary and Confidential

## Slide 6: Naming Conventions
Using C function or variable names in assembly routines and using assembly symbols in C code.
In asm code , to use a C symbol use .extern
Eg: Declaration in ASM  .var temp.;
Usage in C  extern int temp;
Eg: Declaration in C  int temp1;
Usage in ASM  .extern temp1.;
Proprietary and Confidential

## Slide 7: Function Calling
While calling a function from C to assembly we need to declare the function globally in asm.
While calling a function from assembly to C we need to use CALL.
Eg: From C to ASM
In C In ASM
Test(); .global Test.;
.type Test., STT_FUNC;
Test.:
.Test..END
Eg: From ASM to C
In ASM In C
call Test; Test() {
Proprietary and Confidential

## Slide 8: Guidelines to be followed
Function call in C - subroutine in ASM
Include <asm_sprt.h> and <def21569.h> in ASM function
Save and Unsave all the Registers in ASM function
Define them in code memory segment
Declare the function as global
Function call in ASM - subroutine in C
Use function name and call for calling
Note: In C, function can be used without any prefix in Function name
Function call in ASM - subroutine in ASM
Declare the function as global
Terminate the function with rts (Return to Subroutine)
Proprietary and Confidential

## Slide 9: Argument Passing
C run-time environment uses a set of registers and the run-timestack to transfer function parameters to assembly routines
r4 receives the first argument
r8 receives second argument
r12 receives third argument
Remaining parameters of the argument are being passed to stack. They can be retrieved using “reads(n)” instruction
r0 has the return value of the function
Eg : Test(int a , int b , float c)
Proprietary and Confidential

## Slide 10: Argument Passing
Eg: Function calling from C
Int Add(int a, int b) /* Declaration */
c = Add(a,b); /* Function Call */
Function in asm
.global Add.;
.type Add., STT_FUNC;
Add.:
r0 = r4 + r8;
.Add..END
Here r4 contain the value of ‘a’, r8 contain value of ‘b’, and the sum is returned through r0.
Proprietary and Confidential

## Slide 11: Argument Passing
Eg: Function calling from Asm
r4 = 10;
r8 = 12;
call Myfunc;
dm(result.) =r0;
Function in C
        int Myfunc(int n, int m)
        {
        int z;
        z = m + n;
        return z;
        }
Proprietary and Confidential

## Slide 12: Section Definitions
Required sections in LDF:
Seg_pmda :
Program memory data section, declared as 32 bit wide memory
Seg_pmco :
Program memory code section, declared as 48 bit wide memory
Seg_dmda :
Data memory section name, declared as 32 bit wide memory
Seg_stak :
C-Runtime Stack section declaration
Seg_heap :
C-Heap section declaration
Proprietary and Confidential

## Slide 13
Processing Elements - Overview
Two Processing Elements:
- PEx (Primary Processing Element)
- PEy (Secondary Processing Element)
Each Processing Element consist of,
- Data Registers
- ALU (Arithmetic Logic Unit)
- Multiplier
- Shifter
Proprietary and Confidential

## Slide 14
Processing Elements - Overview
Why 2 Processing elements?
How PEy can be Enabled?
Cycles will be reduced
The PEYEN bit (bit 21) in the MODE1 register enables or disables the PEy processing element
Proprietary and Confidential

## Slide 15: SIMD:
SIMD means Single Instruction Multple Data, which means single instruction is applied on multiple data
The SHARC core contains two sets of computational units and associated register files, two processing elements (PEx and PEy) support SIMD operation.
The PEYEN bit in the MODE1 register enables or disables the PEy processing element.
When PEYEN is cleared (0), the processor operates in SISD mode, using only PEx. When the PEYEN bit is set (1), the processor operates in SIMD mode.
Proprietary and Confidential

## Slide 16
Compute Instructions in SIMD Mode
bit set MODE1 PEYEN; /* enable SIMD */
nop; /* effect latency */
R0 = R1 + R2; /* explicit ALU instruction */
S0 = S1 + S2; /* implicit ALU instruction */
F0 = F1 * F2; /* explicit MUL instruction */
SF0 = SF1 * SF2; /* implicit MUL instruction */
R5 = LSHIFT R6 by <data8>; /* explicit shift imm instruction */
S5 = LSHIFT S6 by <data8>; /* implicit shift imm instruction */
Proprietary and Confidential

## Slide 17
QUESTIONS?